## Slide 1
Smart Spreading Factor Assignment for LoRaWANs
Tuğrul Yatağan
yatagan@itu.edu.tr
Thesis Advisor: Prof. Dr. Sema Fatma Oktuğ
Notes: Hello everyone I am going to present my master thesis “Smart Spreading Factor Assignment for LoRaWANs”

## Slide 2
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Outline
Notes: I will start with brief information about LPWAN
Then I will give background information about LoRa and LoRaWAN
I will summarize other recent related works
I will describe proposed smart spreading factor assignment technique
I will explain simulation environment
I will show simulation results

## Slide 3
Introduction: LPWAN Overview
Number of Internet of Things applications increased exponentially in last few years
How to provide connectivity for low power devices distributed over large geographical areas?
Example LPWA application areas:
  Smart city
  Industrial assets monitoring
  Smart grid metering
  Agriculture
  Logistic
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: I will start with explaining lpwan
Number of Internet of Things applications increased exponentially in last few years
How to provide connectivity for low power devices distributed over large geographical areas? Lpwan technologies answer this question
Such LPWAN applications are:
    Smart city
    Industrial assets monitoring
    Smart grid metering
    Agriculture
    Logistic
    Etc.

## Slide 4
Introduction: LPWAN Overview
Key challenges:
  Communication range
    Tens of kilometers
  Device battery life
    Up to 10 years of battery life with a single AA battery
  Scalability
    Hundreds of end devices
  Device cost
    Affordable radio chip
    Low subscription cost
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: What are the key challenges of lpwan technologies?
they are expected to achieve tens of kilometers communication range
they are expected to run up to 10 years of battery life with a single AA battery
they should be able to support and operate hundreds of end devices
And the end device cost should be low, subscription cost should be low too if there is any subscription costs

## Slide 5
Introduction: LPWAN Overview
Introduction
LoRa
Related Works
Proposed Technique
LPWAN fills the technology gap between:
  Short range wireless technologies (ZigBee, Bluetooth, WiFi)
    Range is limited to a few hundred meters at best
    Very costly to deploy dense network
  Cellular (2G, 3G, LTE)
    Optimized for voice and data
    Complex and expensive
    High power consumption
Simulation Environment
Simulation Results
Conclusion
Notes: LPWAN technologies aims to fill the technology gap between short range wireless technologies such as ZigBee, Bluetooth, WiFi and Cellular networks such as 2G, 3G and LTE
Short range wireless technologies
  range is limited to a few hundred meters at best
  And they are very costly to deploy for dense networks
Cellular networks
  are optimized for voice and data
  They are complex and expensive
  They consume too much power

## Slide 6
Introduction: LPWAN Key Features
Low power wide area networks:
Low power
Long range
Low cost
Low data rate
High latency
LPWAN applicable applications:
  Delay tolerant
  Low data rate
  Low power consumption
  Low cost
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: LPWAN technologies offer
  Low power
  Long range
  And low cost
  However they cannot provide high data rate or low latency
To use lpwan, applications should be
  Delay tolerant
  Low data rate
  Low power consumption
  Low cost
LPWAN is not suitable for many industrial IoT, vehicle to vehicle since they require low latency

## Slide 7
Introduction: LPWAN Key Features
Several competing LPWAN technologies:
  LoRa
  Sigfox
  NB-IoT
  LTE-M
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: There are several competing LPWAN technologies well know lpwan technologies are LoRa Sigfox NB-IoT LTE-M
LoRa and Sigfox use license free ISM frequency bands
While NB-IoT and LTE-M use licensed frequency bands which brings extra cost
Both LoRa and Sigfox are known for ultra-low power consumption
While NB-IoT and LTE-M are promoted for higher data rate
LoRaWAN networks can be deployed as a private network like WiFi
However, Sigfox and NB-IoT are only available with operator contract
Focus of this work is on lora

## Slide 8
LoRa: Modulation
LoRa modulates the signals in Sub-GHz ISM band using a proprietary modulation technique based on Chirp Spread Spectrum
Resilient to interference and noise
Chirp is a sinusoidal signal of frequency increase or decrease over time
  The direction of the scan determines the transmission symbol
  The speed of the scan is called the spreading factor (SF)
Higher SF:
Lower data rate
Longer transmission duration
Higher power consumption
Higher resilience to noise
Longer transmission range
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: LoRa modulates the signals in Sub-GHz ISM band using a proprietary modulation technique based on Chirp Spread Spectrum
It is resilient to interference and noise
Chirp is a sinusoidal signal which its frequency increases or decreases over time
  The direction of the scan determines the transmission symbol
  And The speed of the scan is called the spreading factor
increasing spreading factor:
  decreases data rate
  increases transmission duration
  increases power consumption
  However it makes the signal more resilience to noise
  Increases transmission range

## Slide 9
LoRa: Spreading Factor
Ratio between symbol and chirp rate is equal to 2SF
SF can take values between 7 and 12
SF provides tradeoff between data rate, range and power consumption
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: The ratio between symbol and chirp rate is equal to 2SF
  Spreading factor also determines data rate of a LoRa transmission
  Here Rb is bit rate in bps, SF is spreading factor, CR is error correction code rate BW is bandwidth in Hertz
  SF can take values between 7 and 12
  CR can take values between 1 and 4
When bandwidth and code rate are constant as the spreading factor increases, the data rate decreases
Higher spreading factors delivers long range at an expense of lower data rate and high power consumption

## Slide 10
LoRa: Spreading Factor Assignment Issue
Different SF transmissions are orthogonal to each other
  Packets with different SFs in same channel can be received simultaneously
Simultaneous transmissions with same SF may collide
End nodes select SF according to signal strength of the downlink transmission from GW
End nodes which close to the GW will probably select the lowest SF all the time
  Same SF transmission collision
  Number of collisions increases while number of end devices close to the GW increases
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: Simultaneous different spreading factor transmissions are orthogonal to each other
  Which means gateway can simultaneously receive multiple transmissions with different spreading factors
But simultaneous transmissions with the same spreading factor may not be received due to collision
initially, a node is not aware of how far away it is from a gateway. However, it can guess by observing received signal power of a downlink transmission
End nodes which close to the gateway will probably select the lowest spreading factor all the time which results
  Same spreading factor transmission collisions
  collisions increases while number of end devices close to the gateway increases

## Slide 11
LoRa: LoRaWAN
LoRaWAN is open standard MAC layer protocol for LoRa physical layer, developed by LoRa Alliance
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
End Node (EN)
  Low power embedded device that only communicates with gateways
  Class A
    Generates uplink transmission at any time
    Only receives a period of time after an uplink transmission
    Default operation mode
    Suitable for battery powered applications
  Class B
    Periodic receive window
    Suitable for low latency applications
  Class C
    Continuous receive window
    Suitable for no latency applications
Notes: LoRa has an open standard MAC layer protocol called LoRaWAN
  LoRaWAN is developed and maintained by LoRa Alliance which is an non-profit organization
There are three main LoRaWAN network entities, which are end node, gateway and network server
End node is a low power embedded device that only communicates with gateways
LoRaWAN standard defines three classes for end devices
Class A end nodes generate uplink transmission at any time
  And Only receives a period of time after an uplink transmission
  Class A is the default operation mode for end nodes
Class B end nodes extend Class A behavior by adding scheduled periodic receive windows
Class C end nodes extend Class A behavior by keeping receive window open all the time
In this thesis, only Class A end devices are considered since Class A behavior leads to the lowest power consumption and Class A is the default operation mode.

## Slide 12
LoRa: LoRaWAN
Gateway (GW)
  Receive/transmit packets coming from/to end nodes
  Can listen multiple channel at the same time
Network Server (NS)
  Brain of the LoRaWAN network
  Routes messages from application to end nodes
  Process hungry calculations and applications such as triangulation
  Can tweak communication parameters of nodes such as SF and TX power
    Adaptive Data Rate (ADR)
    ADR implementation is left to the network operators
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 2.7: LoRaWAN star of stars network architecture.
Notes: Next entity is gateway
  gateway receives packets coming from end nodes
  gateway can receive from multiple channels at the same time.
  Gateways are usually connected to power grid, so power consumption of a gateway is not critical
Network Server is the brain of the LoRaWAN network
  It routes messages from application to end nodes
  Process hungry calculations and applications can be run in NS such as triangulation
  Network server can tweak communication parameters of nodes such as spreading factor and transmit power
    This is done by Adaptive Data Rate mechanism
    If ADR is enabled, then spreading factor of the end node’s are controlled by the NS.
    But The ADR algorithm is not defined in LoRaWAN protocol.
    They define the protocol but leave ADR algorithm to the network operators.

## Slide 13
LoRa: LoRaWAN
Messages transmitted by end nodes are received by all GWs in range
  Star of stars
No direct communication between end nodes
No forwarding between end nodes
Simplify the design of end devices
  Move complexity to backend system
Pure ALOHA medium access
  End nodes do not check whether the channel is free or not before transmission
  No CSMA/CA
  No waste precious energy in busy-listening to other devices
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 2.7: LoRaWAN star of stars network architecture.
Notes: Messages transmitted by end nodes are received by all GWs in range
  This network architecture is called as star of stars
End nodes cannot communicate with each other thus
End nodes do not make any forwarding
This architecture simplifies the design of end devices
  It moves complexity to backend system
LoRaWAN adopts pure ALOHA medium access
  Which means End nodes do not check whether the channel is free or not before transmission
  There is no Carrier-sense multiple access with collision avoidance mechanism
  End nodes do not waste precious energy by busy-listening the wireless medium

## Slide 14
LoRa: ISM Regulations
LoRaWAN operates in license free Industrial, Scientific, and Medical (ISM) bands
ISM bands are subject to radio transmission time and power regulations
Duty cycle restriction
  Limitation on percentage of air time
  1% duty cycle restriction enforces
    Single transmission cannot exceed 3.6 seconds
    Total time on air in one hour cannot exceed 36 seconds
Effective isotropic radiated power restriction
  Sets maximum allowed transmit power of a transmitter
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: LoRaWAN operates in license free ISM bands.
ISM bands are subject to radio transmission time and power regulations
Duty Cycle Restriction is a limitation on percentage of air time.
  For example 1% duty cycle restriction enforces
  Single transmission cannot exceed 3.6 seconds
  And total time on air in one hour cannot exceed 36 seconds
Effective Isotropic Radiated Power Restriction sets the maximum allowed transmit power of a transmitter

## Slide 15
Related Works
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
“Performance Evaluation of LoRa Networks in a Smart City Scenario”
  ns–3 module to study the performance of a LoRa-based IoT network in a typical urban scenario
  SF assignment has great effect on LoRaWAN network performance
“Impact of LoRa Imperfect Orthogonality: Analysis of Link-Level Performance” and “Scalability Analysis of a LoRa Network under Imperfect Orthogonality”
  Effects of imperfect orthogonality between different LoRa spreading factor transmissions
  Aggregated co-SF and inter-SF interference power SIR distributions to capture the coverage distance from the gateway for modeling interference
Notes: Related literature has started to grow recently
These are some of the notable related works on LoRa spreading factor assignment issue
In “Performance Evaluation of LoRa Networks in a Smart City Scenario”
  Authors created a ns–3 module to study the performance of a LoRa-based IoT network in a typical urban scenario
  They showed that spreading factor assignment has great effect on LoRaWAN network performance
In “Impact of LoRa Imperfect Orthogonality: Analysis of Link-Level Performance” and “Scalability Analysis of a LoRa Network under Imperfect Orthogonality”
  Authors investigated Effects of imperfect orthogonality between different LoRa spreading factor transmissions

## Slide 16
Related Works
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
“EXPLoRa: Extending the performance of LoRa by suitable spreading factor allocations”
  New algorithm for spreading factor assignment in LoRaWANs
  The algorithm assigns spreading factors by balancing air time of the packets in each spreading factor
The adaptive data rate (ADR) algorithm recommended by Semtech utilizes SNR of the last 20 transmissions
  Selects the lowest possible SF and transmit power to maintain reliable communication between end node and gateway
  Current state of the art implementation
Notes: In “EXPLoRa: Extending the performance of LoRa by suitable spreading factor allocations”
  Authors proposed new algorithms for spreading factor assignment
  Proposed algorithm assigns spreading factors by balancing air time of the packets in each spreading factor
Lastly, The adaptive data rate algorithm recommended by Semtech utilizes signal to noise ratio of the last 20 transmissions
  Recommended algorithm selects the lowest possible spreading factor and transmit power to maintain reliable communication between end node and gateway
  It can be said that this is the current state of the art implementation
  The Things Network, one of the biggest LoRaWAN networks in the world, is utilizing this algorithm for their deployed networks

## Slide 17
Proposed Technique: Solution
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Network server can force some of close end nodes to select higher SF
Number of collision may decrease due to the orthogonality of different SF
However, higher SF:
  Higher time on air
  Prone to collision with other higher SF transmissions
Notes: The collision problem I mentioned previously can be solved by forcing some of the close nodes to select higher spreading factors even they are able to communicate with lower spreading factors
Number of collision may decrease due to the orthogonality of different spreading factor
However, higher spreading factor means
  Higher time on air
  And this will increase the probability of collisions with other high spreading factor transmission

## Slide 18
Proposed Technique: Challenge
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Increasing SF may increase the collisions with nodes in other GW's range
  Extra care must be taken for intersection area
How NS should assign SFs to nodes?
It is difficult to propose a single SF assignment rule for every possible topology
  Every network is different
  Optimizing nodes’ SFs requires different rules
Network aware machine learning based SF assignment approach is proposed
Notes: In multiple gateways scenarios, this approach may increase the collisions with the nodes in other gateways’ range
  So extra care should be taken for nodes in the intersection area
Distribution of spreading factor among nodes becomes an important problem
It is difficult to propose a single spreading factor assignment rule for every possible LoRaWAN topology since
  every network is different
  optimizing their nodes’ spreading factors requires different rules
For these reason a network aware machine learning based spreading factor assignment approach is proposed

## Slide 19
Proposed Technique
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
NS can keep track of transmission logs:
  Location
    X and Y coordinates (by triangulation)
  SF
  Transmission result
    Successful
    Interfered
    Under sensitivity
Notes: In this approach, NS can keep track of transmission logs with
  Transmission location. This can be obtained by triangulation
  Spreading factor
  And transmission results. Possible transmission results are
    Successful
    Interfered
    And under sensitivity
You can see sample section of transmission logs

## Slide 20
Proposed Technique
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
NS can train a classifier to predict future transmission result for a specific location and a specific SF
Using this prediction model NS can assign SFs to nodes considering prediction of transmissions
NS can modify SF of a node using existing ADR mechanism
  No change required on LoRaWAN protocol
Every end node makes at least one uplink transmission in a day
  At least one open receive window every day to inform end nodes about new spreading factor
Notes: Using those obtained information, NS can train a classifier to predict future transmission result for a specific node and a specific spreading factor
Using this prediction model NS can assign spreading factors to nodes considering the collision probability.
NS can modify spreading factor of the node using existing ADR mechanism.
  Thus, this technique does not require any modification on LoRaWAN protocol.
It is fair enough to assume that every end node makes at least one uplink transmission in a day
  so there is at least one open receive window every day to inform end nodes about new spreading factor.
  ns cannot just ask end nodes to change spreading factor at any time, ns needs to wait a uplink transmission

## Slide 21
Proposed Technique
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Decision tree classifier (DTC) and support vector machine (SVM) machine learning methods are employed
Mass amount of LoRaWAN transmission logs can be generated using developed simulation tool
A classifier is trained from generated dataset and this classifier is used for selecting optimum SF for the nodes
  NS can create a classifier daily basis
  Gateways can inform nodes to use suggested SF
Notes: In this work, decision tree classifier and support vector machine methods are employed to predict the transmission results
It is possible to generate mass amount of LoRaWAN transmission logs for various topologies using our simulator.
A classifier is trained from generated dataset and this classifier is used for selecting optimum spreading factor for the nodes
  Network server can create a classifier daily basis
  Gateways can inform nodes about to use new spreading factors

## Slide 22
Proposed Technique: Simulation
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
The tool first runs a simulation with random SF scheme
Transmission logs are combined to create the training dataset
The dataset is fed to DTC or SVM classifiers for training
Second simulation is run with the trained classifier
The tool selects optimum SF for transmissions considering transmission predictions
Notes: The tool first runs a simulation with random spreading factor scheme.
After random spreading factor scheme simulation completed, transmission logs are combined into three feature columns one class label column
Then, the dataset is fed to DTC or SVM classifiers for training phase.
Then, Second simulation is run with the trained classifier.
The tool selects optimum spreading factor for transmissions considering transmission predictions

## Slide 23
Proposed Technique: Simulation
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
For every transmission:
  The classifier predicts the transmission result for the lowest possible SF
  If the transmission result is predicted as interfered
    increase SF
    predict a new transmission result
  If new transmission result is classified as successful
    continue to execute with selected SF
  If no SF transmission result is predicted as successful
    select the lowest possible SF
    continue to execute
Notes: For every transmission
  the classifier predicts the transmission result for the lowest possible SF
  If the transmission result is predicted as interfered, then the tool increases the spreading factor and predicts a new transmission result
  If the new transmission result is classified as successful, then simulator continues to execute with selected spreading factor
  If no spreading factor transmission result is predicted as successful, then the tool selects the lowest possible spreading factor again and continue to execute.

## Slide 24
Simulation Environment
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
A discrete event simulation tool is developed to study the effects of various SF strategies for LoRaWANs
  Python
  From scratch
  Open source
Capabilities
  LoRaWAN Class A only
  Uplink transmission only
Notes: For this work a discrete event simulator is developed from scratch in Python to study the effects of various spreading factor strategies
  The tool source code is open source and available at GitHub
Simulator only supports LoRaWAN Class A end devices
  Since Class A behaviour is the default operation mode and provides the lowest power consumption.
  Downlink transmissions are not considered. Since they are rare in real world deployments because of ISM band regulations dictate duty cycle transmission limit for all devices including gateways

## Slide 25
Simulation Environment: Inputs
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Simulation topology inputs:
  radius (m)
  number of nodes
  number of gateways
Notes: Simulator can generate uniformly distributed circular shape network topology with input parameters:
  radius in meter,
  number of nodes
  and number of gateways.
The tool first distributes gateways
Then, randomly places end nodes in network radius.

## Slide 26
Simulation Environment: Inputs
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Simulation inputs:
  simulation duration (s)
  packet size (B)
  packet generation rate (pps)
  SF assignment method
  packet generation type
Notes: Global simulation input parameters are
  simulation duration in second
  packet size in Byte
  packet generation rate in packets per second
  spreading factor assignment method
  And packet generation type which can be
    Periodic and Poisson
    Initial transmission intervals are always generated by Poisson.
    to prevent continuous collisions between periodic transmissions

## Slide 27
Simulation Environment: Outputs
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
  Simulation outputs:
  number of generated packets
  number of successfully received packets
  number of interfered packets
  number of under sensitivity packets
  network packet delivery ratio percentage
  network throughput (bps)
  total transmit energy consumption (J)
Notes: With these inputs the simulator produces
  number of generated packets
  number of successfully received packets
  number of interfered packets
  number of under sensitivity packets
  Network packet delivery ratio percentage,
  network throughput in bits per second
  and total transmit energy consumption in Joule
Simulator also produces prediction accuracy percentage and confusion matrix for machine learning schemes.

## Slide 28
  Link quality of a wireless system [17]:
Sum of system gains and system losses is assumed as +7 dB
All transmissions use maximum allowed transmit power 14 dBm
Simulation Environment: Link Model
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: Link quality of a wireless system can be expressed by the link budget
Link budget can be calculated by this formula where
  PRX is the expected receive power at the receiver
  PTX is the transmit power of the transmitter
  G SYS is the system gains such as transmitter and receiver antenna gains
  L SYS is the system losses such as transmitter and receiver line, circuit, antenna losses
  L PATH is the propagation path loss between transmitter and receiver antennas in open space
it is assumed that sum of system gains and system losses is +7 dB
it is assumed that nodes always select maximum allowed transmit power, which is 14 dBm.
If the received signal power is higher than the gateway sensitivity,
then signal can be decoded by the receiver successfully when there is no interfering transmission.

## Slide 29
  Free space propagation loss [32]:
  Assume h = 15 m and f = 868 MHz
Simulation Environment: Link Model
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: Free space propagation loss is calculated as
  Where h is the gateway altitude and f is the frequency of the signal,
  It is assumed that gateway altitude is 15 m and frequency is 868 MHz which is European ISM band frequency
With these assumptions, propagation loss calculation become

## Slide 30
Simulation Environment: Interference Model
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
It is assumed that there is no other technology interference
Simulator calculates the effect of different SF transmissions to each other
  Signal to interference plus noise ratio threshold matrix [33]:
  Margin between referenced signal and interfering signal to correctly decode the referenced signal
Notes: In this work, it is assumed that there is no other technology interference in the network except LoRa interference
Simulator calculates the effect of different spreading factor transmissions to each other
signal to interference plus noise ratio threshold matrix is adopted
  Where T ij is margin between referenced signal with SF = i and interfering signal with SF = j to correctly decode the referenced signal

## Slide 31
Simulation Environment: Interference Model
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
If there are more than one interfering signal
  Cumulative sum of all interfering signal received power for each SF
  SINR threshold can be calculated
Packet survives from all interferences if:
Notes: If there are more than one interfering signal, referenced signal must satisfy the margin for sum of all interfering signal received power for each spreading factor
SINR threshold can be calculated by this equation
  Where Prc,0 is received signal power of referenced signal
  Prc,l is received signal power of interfering signal for SF = j.
If a packet with SF = i satisfies the following condition for every SF = j, then packet is survived from all interferences.

## Slide 32
Simulation Environment: Software
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Tool keeps an event queue
Every event is a transmission
Every transmission has
  Time
  SF
  Source
  Duration
  Status
Simulation steps:
  Every node generates an event according to their traffic generation rate
  Initially all events are in pending state
  Tool executes events
  Tool marks events statuses as transmitted, interfered or under sensitivity
  Tool calculates network PDR, throughput and transmit energy consumption
Example CLI command:
python3 main.py -r 7000 -g 3 -n 300 -s SF_Lowest -d 3600
Notes: The tool keeps a transmission queue
Every event in this queue is a transmission
Every transmission has
  time
  spreading factor
  source
  Duration
  and status fields
First
  Every end node generates an event according to their traffic generation rate and inserts this event to event queue.
  Initially all events are in pending state
  Tool executes events one by one
  Tool marks events statuses as transmitted, interfered or under sensitivity
  Finally tool calculates network PDR, throughput and transmit energy consumption
A command line parser is developed for interacting with the tool, so the tool can be run without any programming or scripting
  Example tool command is below

## Slide 33
Simulation Environment: Software
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: Simulation class is the core class of the simulator.
Event queue is in this class and packet class is the instances of this queue
Every simulation instance has topology instance and every topology instance has several node and gateway objects

## Slide 34
Simulation Results: Single Gateway
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 6.1 : PDR plot for various spreading factors. (r = 3000 m, GW = 1, Rt = 0.01 pps)
(a) PDR
(b) Transmit energy
Notes: For the remaining simulation results presented:
  packet size is set to 60 Bytes
  traffic generation type is set as Poisson
First, I will present single gateway and multiple gateway simulation results to show correctness of the simulator then I will present smart spreading factor simulation results
Here PDR and transmit energy consumption plots of various spreading factor assignment schemes are shown
Increasing spreading factors, increases time on air
This increases the number of collisions thus decreases the PDR
Also, increasing spreading factors increases total transmit energy consumption as expected
High spreading factors gives poor PDR results as the number of nodes increases

## Slide 35
Simulation Results: Single Gateway
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 6.2 : PDR plot for various spreading radii. (GW = 1, SF = SF_Lowest, Rt = 0.01 pps)
(a) PDR
(b) Transmit energy
Notes: plots for various network radii are shown
lowest spreading factor assignment scheme is used for these plots
Increasing network radius,
  increases the number of under sensitivity transmissions
  thus decreases the PDR
Nodes select higher spreading factors when they are far away from the gateway.
  Thus, higher spreading factor leads to
  longer air time,
  higher number of collisions
  and higher total transmit power consumption

## Slide 36
Simulation Results: Single Gateway
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 6.3 : PDR plot for various packet generation rates. (r = 3000 m, GW = 1, SF = SF_Lowest)
(a) PDR
(b) Transmit energy
Notes: plots for various packet generation rate are shown
Increasing packet generation rate,
  increases air time
  thus increases number of collisions,
  decreases PDR
  and increases transmit power consumption
Doubling packet generation rate doubles total transmit power consumption

## Slide 37
Simulation Results: Multiple Gateway
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 6.4 : PDR plot for various number of gateways. (r = 3000 m, SF = SF_Lowest, Rt = 0.01 pps)
(a) PDR
(b) Transmit energy
Notes: plots for various number of gateways are shown
Increasing number of gateways in constant topology radius,
  decreases the distance between nodes and gateways
  Thus, decreases the number of collisions at gateways
  Hence, increases the PDR.
Since topology radius is small, most of the end nodes selects lowest spreading factor all the time
  Thus air time is same and total transmit power consumption is same for all plots

## Slide 38
Simulation Results: Smart SF Schemes
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Figure 6.5 : PDR plot for lowest and smart spreading factor schemes. (r = 5000 m, GW = 3, Rt = 0.01 pps)
(a) PDR
(b) Transmit energy
Notes: Finally plots for the smart spreading factor schemes are shown, these plots are main objective and main results of this work
network radius is set to 5000 meters, number of gateways is set to 3
Prediction model needs nodes' locations and three gateways are enough to locate position of nodes by triangulation.
Both smart SVM and smart DTC schemes give better PDR than lowest spreading factor schemes when number of nodes increases.
Increasing number of nodes, increases number of interferences.
Smart schemes can only improve network performance when LoRa interference is high.
Moreover, smart schemes give better results when nodes are deployed closer to the gateway, since nodes have margin to increase their spreading factors when they are deployed closer to the gateway
If a node is far away from gateway, then smart schemes cannot increase the spreading factor to avoid interference since the assigned spreading factor is already high.
As number of nodes increases, both smart SVM and smart DTC schemes consume slightly more energy than lowest spreading factor scheme,
however they give better PDR results in return
Random spreading factor scheme consumes much higher transmit power than the rest.

## Slide 39
Prediction accuracy is not directly proportional to network PDR
Correct prediction of an interfered transmission may not increase the PDR but increases the prediction accuracy
Simulation Results
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: prediction accuracy of smart SVM and smart DTC schemes are presented for various network radii and number of nodes.
Prediction accuracy is not directly proportional to network PDR
Correct prediction of an interfered transmission may not increase the PDR but increases the prediction accuracy
Smart DTC gives better network PDR results than smart SVM, even overall smart SVM prediction accuracy is higher
The distribution of different labeled data points in the dataset is strongly related to simulation parameters.
If simulation is run with small topology radius and high number of nodes, then number of interfered transmission labeled data points increases.
On the other hand, using a large topology radius in the simulation causes the number of under sensitivity transmission labeled data points to increase.
Moderately dense network parameters are chosen to make it closer to real world deployments.
With the simulation parameters utilized in this section, simulation tool usually produces imbalanced dataset.
Number of under sensitivity transmission labeled data points are less than number of successful transmission labeled data points.
Besides, number of interfered transmission labeled data points are even less than number of under sensitivity transmission labeled data points. In this case, smart DTC predicts interfered transmission labeled data points more accurately.
Correct classification of interfered transmissions yields better network PDR results, thus smart DTC scheme gives better network PDR results.

## Slide 40
Conclusion
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
SF assignment on network performance is investigated in detail
Factors that increase the number of collisions are evaluated
Measures that can be taken to reduce collisions are described
A discrete event simulator is developed from scratch to study SF assignment strategies
A novel method which utilizes machine learning techniques is proposed
Simulation results show smart SF methods provide promising network performance improvements especially for dense LoRaWAN networks
Notes: To summarize, in this work
Spreading factor assignment on network performance is investigated in detail
Factors that increase the number of collisions are evaluated
Measures that can be taken to reduce collisions are described
A discrete event simulator is developed from scratch to study Spreading factor assignment strategies
A novel method which utilizes machine learning techniques is proposed
Simulation results show smart Spreading factor methods provide promising network performance improvements especially for dense LoRaWAN networks

## Slide 41
Conclusion
Introduction
LoRa
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
As for future work
  Transmit power optimization
  Class B and Class C end node behavior
  Other machine learning methods such as reinforcement learning
  Other transmission parameters such as node id and transmission time can be included
Summary of this work is accepted to ISCC 2019 Barcelona, Spain
  Yatagan, T. and Oktug S., 2019, Smart Spreading Factor Assignment for LoRaWANs, 2019 IEEE Symposium on Computers and Communications (IEEE ISCC 2019)
Notes: As for future work,
  transmit power optimization can be included to the proposed smart schemes
    In this thesis, it is assumed that nodes always use maximum transmit power for uplink transmission, however nodes close to gateways can decrease transmit power to save energy
  it is also assumed that only LoRaWAN Class A end nodes are present, however Class B and Class C end node behavior can be integrated to check how extra downlink communication effects smart SF schemes
  Moreover, other machine learning methods can be investigated. Reinforcement learning could be a good candidate.
  Also, other transmission parameters such as node id and transmission time can be included to the proposed scheme in order to improve prediction performance
Lastly summary paper of this work is accepted to IEEE ISCC 2019 and will be presented in Barcelona, Spain at Second of July

## Slide 42
Notes: Thank you for your attention.

## Slide 43
References
European Telecommunications Standards Institute (2018). Electromagnetic compatibility and Radio spectrum Matters (ERM); Short Range Devices (SRD); Radio equipment to be used in the 25 MHz to 1 000 MHz frequency range with power levels ranging up to 500 mW EN 300 220-1 V2.4.1, Technical Report, European Telecommunications Standards Institute, Sophia Antipolis, France, https://www.etsi.org/deliver/etsi_en/300200_300299/30022002/03.02.01_60/en_30022002v030201p.pdf [Accessed: 03-May-2019].
LoRa Alliance Technical Committee Regional Parameters Workgroup(2018). LoRaWAN 1.1 Regional Parameters v1.1rB, Technical Report, LoRa Alliance, San Ramon, California, USA, https://lora-alliance.org/sites/default/files/2018-04/lorawantm_regional_parameters_v1.1rb_-_final.pdf [Accessed: 03-May-2019].
Semtech Corporation Wireless Sensing and Timing Products Division (2019). SX1276/77/78/79 - 137 MHz to 1020 MHz Low Power Long Range Transceiver Datasheet, Technical Report, Semtech Corporation, Camarillo, California, USA, https://www.semtech.com/uploads/documents/DS_SX1276-7-8-9_W_APP_V6.pdf [Accessed: 03-May-2019].
Egli, P., (2017). LPWAN - Low Power Wide Area Networks, http://peteregli.net/content/mobile-wireless/LPWAN/LPWAN.pdf [Accessed: 03-May-2019].
Ghoslya, S., (2017), LoRa: Symbol Generation, https://www.sghoslya.com/p/lora-is-chirp-spread-spectrum.html [Accessed: 03-May-2019].
Witekio, (2018), LoRaWan, a dedicated IoT network, https://witekio.com/blog/lorawan-dedicated-iot-network [Accessed: 03-May-2019].
Sornin, N. and Yegin, A. (2017). LoRaWAN 1.1 Specification, Technical Report, LoRa Alliance, Beaverton, Oregon, USA, https://lora-alliance.org/sites/default/files/2018-04/lorawantm_specification_-v1.1.pdf [Accessed: 03-May-2019].
Centenaro, M., Vangelista, L., Zanella, A. and Zorzi, M. (2016). Long-range communications in unlicensed bands: the rising stars in the IoT and smart city scenarios, IEEE Wireless Communications, 23(5), 60–67.
Al-Fuqaha, A., Guizani, M., Mohammadi, M., Aledhari, M. and Ayyash, M. (2015). Internet of Things: A Survey on Enabling Technologies, Protocols, and Applications, IEEE Communications Surveys Tutorials, 17(4), 2347–2376.
Raza, U., Kulkarni, P. and Sooriyabandara, M. (2017). Low Power Wide Area Networks: An Overview, IEEE Communications Surveys Tutorials, 19(2), 855–873.
Finnegan, J. and Brown, S. (2018). A Comparative Survey of LPWA Networking, CoRR, abs/1802.04222.
Abramson, N. (1970). THE ALOHA SYSTEM: Another Alternative for Computer Communications, Proceedings of the November 17-19, 1970, Fall Joint Computer Conference, AFIPS ’70 (Fall), ACM, New York, NY, USA, pp.281–285, http://doi.acm.org/10.1145/1478462.1478502.
Sigfox (2017). Sigfox Technical Overview, Technical Report, Sigfox, Labège, France, https://storage.sbg1.cloud.ovh.net/v1/AUTH_669d7dfced0b44518cb186841d7cbd75/dev_medias/build_technicalOverview.pdf [Accessed: 03-May-2019].
Georgiou, O. and Raza, U. (2017). Low Power Wide Area Network Analysis: Can LoRa Scale?, IEEE Wireless Communications Letters, 6(2), 162–165.
Semtech Corporation, Semtech Corporation Website, https://www.semtech.com [Accessed: 03-May-2019].
Berni, A. and Gregg, W. (1973). On the Utility of Chirp Modulation for Digital Signaling, IEEE Transactions on Communications, 21(6), 748–751.
Semtech Corporation Wireless Sensing and Timing Products Division (2015). LoRaTM Modulation Basics AN1200.22, Technical Report, Semtech Corporation, Camarillo, California, USA, https://www.semtech.com/uploads/documents/an1200.22.pdf [Accessed: 03-May-2019].

## Slide 44
References
Adelantado, F., Vilajosana, X., Tuset-Peiro, P., Martinez, B., Melia-Segui, J. and Watteyne, T. (2017). Understanding the Limits of LoRaWAN, IEEE Communications Magazine, 55(9), 34–40.
LoRa Alliance, LoRa Alliance Website, https://lora-alliance.org [Accessed: 03-May-2019].
Magrin, D., Centenaro, M. and Vangelista, L. (2017). Performance evaluation of LoRa networks in a smart city scenario, 2017 IEEE International Conference on Communications (ICC), pp.1–7.
Van den Abeele, F., Haxhibeqiri, J., Moerman, I. and Hoebeke, J. (2017). Scalability Analysis of Large-Scale LoRaWAN Networks in ns-3, IEEE Internet of Things Journal, 4(6), 2186–2198.
Croce, D., Gucciardo, M., Mangione, S., Santaromita, G. and Tinnirello, I. (2018). Impact of LoRa Imperfect Orthogonality: Analysis of Link-Level Performance, IEEE Communications Letters, 22(4), 796–799.
Mahmood, A., Sisinni, E., Guntupalli, L., Rondón, R., Hassan, S.A. and Gidlund, M. (2018). Scalability Analysis of a LoRa Network under Imperfect Orthogonality, IEEE Transactions on Industrial Informatics, 1–1.
Cuomo, F., Campo, M., Caponi, A., Bianchi, G., Rossini, G. and Pisani, P. (2017). EXPLoRa: Extending the performance of LoRa by suitable spreading factor allocations, 2017 IEEE 13th International Conference on Wireless and Mobile Computing, Networking and Communications (WiMob), pp.1–8.
Haxhibeqiri, J., Van den Abeele, F., Moerman, I. and Hoebeke, J. (2017). LoRa Scalability: A Simulation Model Based on Interference Measurements, Sensors, 17(6), http://www.mdpi.com/1424-8220/17/6/1193.
Slabicki, M., Premsankar, G. and Di Francesco, M. (2018). Adaptive configuration of lora networks for dense IoT deployments, NOMS 2018 - 2018 IEEE/IFIP Network Operations and Management Symposium, pp.1–9.
Semtech Corporation (2016). LoRaWAN – simple rate adaptation recommended algorithm, Technical Reportv1.0, Semtech Corporation, Camarillo, California, USA.
The Things Network, (2018), LoRaWAN Adaptive Data Rate, https://www.thethingsnetwork.org/docs/lorawan/adr.html [Accessed: 03-May-2019].
Alpaydin, E. (2010). Introduction to Machine Learning, The MIT Press, 2nd edition.
Yatagan, T., (2019), tugrulyatagan/simlorasf, https://doi.org/10.5281/zenodo.3072925 [Accessed: 03-May-2019].
Yates, R.D. and Goodman, D.J. (2014). Probability and Stochastic Processes: A Friendly Introduction for Electrical and Computer Engineers, Wiley, 3rd edition.
European Telecommunications Standards Institute (2016). Radio Frequency (RF) system scenarios TR 136 942 V13.0.0, Technical Report, European Telecommunications Standards Institute, Sophia Antipolis, France, https://www.etsi.org/deliver/etsi_tr/136900_136999/136942/13.00.00_60/tr_136942v130000p.pdf [Accessed: 03-May-2019].
Goursaud, C. and Gorce, J.M. (2015). Dedicated networks for IoT : PHY / MAC state of the art and challenges, EAI endorsed transactions on Internet of Things, https://hal.archives-ouvertes.fr/hal-01231221.
Python Software Foundation, Python Downlaod Website, https://www.python.org/downloads [Accessed: 03-May-2019].