## Slide 1: ON MODERN DNS BEHAVIOR AND PROPERTIES
Mustafa UÇAR 040100113
Tuğrul YATAĞAN 040100117
Emre GÖKREM 040100124

## Slide 2: Information About Paper
Authors
  Thomas Callahan Case Western Reserve University, Cleveland, OH, USA
  Mark Allman International Computer Science Institute, Berkeley, CA, USA
  Michael Rabinovich Case Western Reserve University, Cleveland, OH, USA
Publication
  ACM SIGCOMM Computer Communication Review
  Volume 43 Issue 3, July 2013
  Pages 7-15

## Slide 3: Information About Paper
Aim of Study
DNS is an important part of that latency, both in contributing to initial connection setup latency but also in picking a server that has low network distance and low load for the client to use
Study Environment
  14 months
  90 home neighborhood in the US
  Served by bi-directional 1 Gbps fiber links
  200 million DNS queries and 1.1 billion flows

## Slide 4: Introduction
What is DNS
  Domain Name System (DNS) is a distributed, hierarchical naming system. The DNS calls for organizational name
Working Principle
  www.google.com
CSZ
  For this study researchers monitor DNS traffic within the “Case Connection Zone”, which is an experimental network

## Slide 5: DNS Requests
Communication across the Internet generally starts with a DNS
Some applications continue to heavily rely on DNS
DNS query types in studied dataset;
  A records are used to map a domain name to an IPv4 address
  AAAA records are used to map a domain to an IPv6 address
  PTR records are also called Reverse DNS records

## Slide 6: DNS Requests
Researchers note that roughly 97% of the DNS requests they observe traverse one of the two local resolvers provided for CCZ clients
The primary resolver is used for approximately 81%, secondary resolver handles 16%
Google’s public DNS resolver handles just over 1% of the requests are observed in paper

## Slide 7: DNS Responses
TTLs (Time to Live)
The Time-To-Live is assigned by the authoritative DNS server and indicates the time period for which the response is valid
The TTL aims to provide consumers with the ability to cache the result of a lookup such that future requests for the same name can be handled locally

## Slide 8: DNS Responses
TTLs (Time to Live)
Longer TTL values allow for higher cache hit rates and decreased DNS traffic
Lower TTL values allow a service provider more agility in terms of changing their mappings and directing traffic
Popular TTL values in the CCZ network, 20 seconds, 60 seconds, 1 hour
Roughly 1% of the TTLs exceed one day, roughly 40% of the hostnames have TTLs of at most 1 minute

## Slide 9: DNS Responses
Equivelant Answers
Individual DNS responses may contain multiple mappings in response to a single query
  Multiple IP addresses give clients recourse if they cannot communicate with a particular IP address
  This aids load balancing across a set of replicas as recursive DNS servers will rotate the order of the IP addresses

## Slide 10: DNS Responses
Proximity
The geographic distance between returned IP addresses and the requesting user device is researched
Popular services attempt to provide content from nearby servers
Directing traffic via DNS is a popular way to drive clients to close servers

## Slide 11: DNS Responses
Proximity
Since DNS responses can have multiple answers;
  For each DNS response they calculate the average distance to each position in the response
  Researchers find the distance quantiles are the same regardless of position in the DNS response

## Slide 12: Transmission
It is observed that two-third of the transactions are completed in under 1 millisecond. This means that these DNS requests are being serviced from the cache.
%10 of the transactions take approximately 10 milliseconds. These are probably associated with traffic to nearby institutions.
Remaining %25 of the transactions completion time are well spread between 10 milliseconds and 1 second. These are transactions that have to make their way through the global DNS ecosystem.

## Slide 13: Utilizing Responses
Use of DNS Responses
Researches stated that, DNS responses often contain more than one IP address for a particular hostname.
In Principle, these IP addresses are equivalent and clients can use any of the set.
Then, IP addresses that clients actually use in subsequent communication are investigated.

## Slide 14: Utilizing Responses
Use of DNS Responses
It is understood that more than %60 of the connections are made to the first IP address listed in the response across al the response sizes except responses with five addresses.
Even in five addresses case, first IP address is used just under %60 of the subsequent connections.
Also, responses with 3 or 6 IP addresses, use of other than first address is uniformly distributed.

## Slide 15: Utilizing Responses
TTLs (Time to Live)
Researches next focused on how well clients honour the TTLs given in DNS responses. Previous work showed that about %47 of the clients violates the TTL.
Findings shows that 8-30% of connection utilize expired DNS records across several datasets from different vantage points.
In research dataset it is found that 13.7% of TCP connections use addresses from expired DNS responses.

## Slide 16: Utilizing Responses
TTLs (Time to Live)
While roughly 55% of hostnames have TTLs of at most 350 seconds, researchers find that 68% of connections and 87% of traffic volume is associated with DNS records with TTLs of at most 350 seconds.
Further, while 80% of hostnames have TTLs of at most one hour, they find that 85% of connections and 95% of bytes associate with DNS TTLs of at most one hour.

## Slide 17: Thank you for listening!