## Slide 1
Smart Spreading Factor Assignment for LoRaWANs
Tugrul Yatagan
yatagan@itu.edu.tr
Sema Oktug
oktug@itu.edu.tr
Department of Computer Engineering
Istanbul Technical University
Istanbul, Turkey
Notes: Good afternoon my name is Tugrul and I am going to present “Smart Spreading Factor Assignment for LoRaWANs” this work is a part of my master thesis. My adviser is prof sema oktug

## Slide 2
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Outline
Notes: This is the outline for my presentation

## Slide 3
Introduction: LPWAN Overview
How to provide connectivity for low power devices distributed over large geographical areas?
Key challenges:
  Communication range
    Tens of kilometers
  Device battery life
    Up to 10 years of battery life with a single AA battery
  Scalability
    Hundreds of end devices
  Device cost
    Affordable radio chip
    Low subscription cost
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: I will start with explaining lpwan
How to provide connectivity for low power devices distributed over large geographical areas? Lpwan technologies answer this question
What are the key challenges of lpwan technologies?
  they are expected to achieve tens of kilometers communication range
  they are expected to be low power
  they should be able to support and operate hundreds of end devices
  And the end device cost should be low

## Slide 4
Introduction: LPWAN
Several competing LPWAN technologies:
  LoRa
  Sigfox
  NB-IoT
  LTE-M
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: There are several competing LPWAN technologies well know lpwan technologies are LoRa Sigfox NB-IoT LTE-M
LoRa and Sigfox use license free ISM frequency bands
While NB-IoT and LTE-M use licensed frequency bands which brings extra cost
Both LoRa and Sigfox are known for ultra-low power consumption
While NB-IoT and LTE-M are promoted for higher data rate
Focus of this work is on lora

## Slide 5
LoRa: Modulation
LoRa modulates the signals in Sub-GHz ISM band using a proprietary modulation technique based on Chirp Spread Spectrum
  Developed by Semtech
Resilient to interference and noise
Chirp is a sinusoidal signal of frequency increase or decrease over time
  The speed of the scan is called the spreading factor (SF)
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: LoRa modulates the signals in Sub-GHz ISM band using a proprietary modulation technique based on Chirp Spread Spectrum
It is resilient to interference and noise
Chirp is a sinusoidal signal which its frequency increases or decreases over time
  And the speed of the scan is called the spreading factor
increasing spreading factor:
  decreases data rate
  increases transmission duration
  increases power consumption
  However it makes the signal more resilience to noise
  Thus increases transmission range
Spreading factor determines data rate of a LoRa transmission
  Here Rb is bit rate in bps, SF is spreading factor, CR is error correction code rate BW is bandwidth in Hertz
  SF can take values between 7 and 12
  CR can take values between 1 and 4
When bandwidth and code rate are constant as the spreading factor increases, the data rate decreases
Higher spreading factors delivers long range at an expense of lower data rate and high power consumption

## Slide 6
LoRa: Modulation
Higher SF:
Lower data rate
Longer transmission duration
Higher power consumption
Higher resilience to noise
Longer transmission range
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
1. Image Source: https://www.sghoslya.com/p/lora-is-chirp-spread-spectrum.html
Fig. A: Spectrogram of various spreading factors (SF7 to SF12). [1]
Notes: LoRa modulates the signals in Sub-GHz ISM band using a proprietary modulation technique based on Chirp Spread Spectrum
It is resilient to interference and noise
Chirp is a sinusoidal signal which its frequency increases or decreases over time
  And the speed of the scan is called the spreading factor
increasing spreading factor:
  decreases data rate
  increases transmission duration
  increases power consumption
  However it makes the signal more resilience to noise
  Thus increases transmission range
Spreading factor determines data rate of a LoRa transmission
  Here Rb is bit rate in bps, SF is spreading factor, CR is error correction code rate BW is bandwidth in Hertz
  SF can take values between 7 and 12
  CR can take values between 1 and 4
When bandwidth and code rate are constant as the spreading factor increases, the data rate decreases
Higher spreading factors delivers long range at an expense of lower data rate and high power consumption

## Slide 7
LoRa: Spreading Factor Assignment Issue
Different SF transmissions are orthogonal to each other
  Packets with different SFs in same channel can be received simultaneously
Simultaneous transmissions with same SF may collide
End nodes select SF according to signal strength of the downlink transmission from GW
End nodes which close to the GW will probably select the lowest SF all the time
  Same SF transmission collision
  Number of collisions increases while number of end devices close to the GW increases
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Fig. 1: Collision between nodes close to the gateway.
Notes: Simultaneous different spreading factor transmissions are orthogonal to each other
  Which means gateway can simultaneously receive multiple transmissions with different spreading factors
But simultaneous transmissions with the same spreading factor may not be received due to collision
initially, a node is not aware of how far away it is from a gateway. However, it can guess by observing received signal power of a downlink transmission
End nodes which close to the gateway will probably select the lowest spreading factor all the time which results
  Same spreading factor transmission collisions
  collisions increases while number of end devices close to the gateway increases

## Slide 8
LoRaWAN
LoRaWAN is open standard MAC layer protocol for LoRa physical layer, developed by LoRa Alliance
End Node (EN)
  Low power embedded device that only communicates with gateways
  End nodes cannot communicate with each other
  End nodes do not check whether the channel is free or not before transmission
    Pure ALOHA medium access
  Class A
    Generates uplink transmission at any time
    Only receives a period of time after an uplink transmission
    Default operation mode
    Suitable for battery powered applications
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: LoRa has an open standard MAC layer protocol called LoRaWAN
There are three main LoRaWAN network entities, which are end node, gateway and network server
End node is a low power embedded device that only communicates with gateways
End nodes cannot communicate with each other
End nodes work in pure ALOHA manner
LoRaWAN standard defines three classes for end devices
Class A end nodes generate uplink transmission at any time
  And Only receives a period of time after an uplink transmission
  Class A is the default operation mode for end nodes
In this work, only Class A end devices are considered since Class A behavior leads to the lowest power consumption and Class A is the default operation mode.
Class B end nodes extend Class A behavior by adding scheduled periodic receive windows
Class C end nodes extend Class A behavior by keeping receive window open all the time

## Slide 9
LoRaWAN
Gateway (GW)
  Receive/transmit packets coming from/to end nodes
  Messages transmitted by end nodes are received by all GWs in range
Network Server (NS)
  Brain of the LoRaWAN network
  Process hungry calculations and applications such as triangulation
  Can tweak communication parameters of nodes such as SF and TX power
    Adaptive Data Rate (ADR)
    ADR algorithm implementation is left to network operators
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Fig. B: LoRaWAN architecture.
Notes: Next entity is gateway
  gateway receives packets coming from end nodes
  Messages transmitted by end nodes are received by all GWs in range
Network Server is the brain of the LoRaWAN network
  Process hungry calculations and applications can be run in NS such as triangulation
  Network server can tweak communication parameters of nodes such as spreading factor and transmit power
    This is done by Adaptive Data Rate mechanism
    If ADR is enabled, then spreading factor of the end node’s are controlled by the NS.
    But The ADR algorithm is not defined in LoRaWAN protocol.
    ADR algorithm implementation is left to the network operators.

## Slide 10
Related Works
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
“Performance Evaluation of LoRa Networks in a Smart City Scenario” [5]
  ns–3 module to study the performance of a LoRa-based IoT network in a typical urban scenario
  SF assignment has great effect on LoRaWAN network performance
“Impact of LoRa Imperfect Orthogonality: Analysis of Link-Level Performance” and “Scalability Analysis of a LoRa Network under Imperfect Orthogonality” [7] and [8]
  Effects of imperfect orthogonality between different LoRa spreading factor transmissions
  Aggregated co-SF and inter-SF interference power SIR distributions to capture the coverage distance from the gateway for modeling interference
The adaptive data rate (ADR) algorithm recommended by Semtech utilizes SNR of the last 20 transmissions [9]
  Selects the lowest possible SF and transmit power to maintain reliable communication between end node and gateway
  Current state of the art implementation
Notes: Related literature has started to grow recently
These are some of the notable related works on LoRa spreading factor assignment issue
In this [5]
  Authors created a ns–3 module to study the performance of a LoRa-based IoT network in a typical urban scenario
  They showed that spreading factor assignment has great effect on LoRaWAN network performance
In these tow paper [7] and [8]
  Authors investigated Effects of imperfect orthogonality between different LoRa spreading factor transmissions
The adaptive data rate algorithm recommended by Semtech utilizes signal to noise ratio of the last 20 transmissions
  Recommended algorithm selects the lowest possible spreading factor and transmit power to maintain reliable communication between end node and gateway
  It can be said that this is the current state of the art implementation
  The Things Network, one of the biggest LoRaWAN networks in the world, is utilizing this algorithm for their deployed networks

## Slide 11
Proposed Technique: Solution
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Network server can force some of close end nodes to select higher SF
Number of collision may decrease due to the orthogonality of different SF
However, higher SF:
  Higher time on air
  Prone to collision with other higher SF transmissions
Fig. 2: Collision avoidance by using higher SF for nodes close to the gateway.
Notes: The collision problem I mentioned previously can be solved by forcing some of the close nodes to select higher spreading factors even they are able to communicate with lower spreading factors
Number of collision may decrease due to the orthogonality of different spreading factor
However, higher spreading factor means
  Higher time on air
  And this will increase the probability of collisions with other high spreading factor transmission

## Slide 12
Proposed Technique: Challenge
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Increasing SF may increase the collisions with nodes in other GW's range
  Extra care must be taken for intersection area
How NS should assign SFs to nodes?
It is difficult to propose a single SF assignment rule for every possible topology
  Every network is different
  Optimizing nodes’ SFs requires different rules
Network aware machine learning based SF assignment approach is proposed
Fig. 3: Collision avoidance for intersecting gateways.
Notes: In multiple gateways scenarios, this approach may increase the collisions with the nodes in other gateways’ range
  So extra care should be taken for nodes in the intersection area
Distribution of spreading factor among nodes becomes an important problem
It is difficult to propose a single spreading factor assignment rule for every possible LoRaWAN topology since
  every network is different
  optimizing their nodes’ spreading factors requires different rules
For these reason a network aware machine learning based spreading factor assignment approach is proposed

## Slide 13
Proposed Technique
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
NS can keep track of transmission logs:
  Location
    X and Y coordinates (by triangulation)
  SF
  Transmission result
    Successful
    Interfered
    Under sensitivity
Table A: Sample section of a transmission dataset.
Notes: In this approach, NS can keep track of transmission logs with
  Transmission location.
  Spreading factor
  And transmission results. Possible transmission results are
    Successful
    Interfered
    And under sensitivity
You can see sample section of transmission logs

## Slide 14
Proposed Technique
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
NS can train a classifier to predict future transmission result for a specific location and a specific SF
  Decision tree classifier (DTC) and support vector machine (SVM) machine learning methods
Using this prediction model NS can calculate new SFs considering prediction of transmissions
  If a transmission result is predicted as interfered
    increase SF
    predict a new transmission result
Notes: Using those obtained information, NS can train a classifier to predict future transmission result for a specific node and a specific spreading factor
  decision tree classifier and support vector machine methods are employed to predict the transmission results
Using this prediction model NS can assign spreading factors to nodes considering the collision probability.
  If the transmission result is predicted as interfered, then the tool increases the spreading factor and predicts a new transmission result

## Slide 15
Proposed Technique
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
NS can modify SF of a node using existing ADR mechanism
  No change required on LoRaWAN protocol
Every end node makes at least one uplink transmission in a day
  At least one open receive window every day to inform end nodes about new spreading factor
Notes: NS can modify spreading factor of the node using existing ADR mechanism.
  Thus, this technique does not require any modification on LoRaWAN protocol.
It is fair enough to assume that every end node makes at least one uplink transmission in a day
  so there is at least one open receive window every day to inform end nodes about new spreading factor.

## Slide 16
Proposed Technique: Simulation
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
The tool first runs a simulation with random SF scheme
Transmission logs are combined to create the training dataset
The dataset is fed to DTC or SVM classifiers for training
Second simulation is run with the trained classifier
The tool selects new SF for transmissions considering transmission predictions
Notes: The tool first runs a simulation with random spreading factor scheme.
After random spreading factor scheme simulation completed, transmission logs are combined into three feature columns one class label column
Then, the dataset is fed to DTC or SVM classifiers for training phase.
Then, Second simulation is run with the trained classifier.
The tool selects new spreading factor for transmissions considering transmission predictions

## Slide 17
Simulation Environment
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Discrete event simulation tool is developed to study the effects of various SF strategies for LoRaWANs
  Python
  From scratch
  Open source
Capabilities
  LoRaWAN Class A only
  Uplink transmission only
Notes: For this work a discrete event simulator is developed from scratch in Python to study the effects of various spreading factor strategies
  The tool source code is open source and available at GitHub
Simulator only supports LoRaWAN Class A end devices
  Since Class A behaviour is the default operation mode and provides the lowest power consumption.
  Downlink transmissions are not considered. Since they are rare in real world deployments because of ISM band regulations dictate duty cycle transmission limit for all devices including gateways
The tool is designed to simulate smart spreading factor schemes, thus machine learning libraries are integrated to the tool. Integrating smart spreading factor schemes to the existing LoRa/LoRaWAN simulation tools such as ns-3 would require major changes. Thus, the tool is designed and developed from scratch to make it easier to integrate smart spreading factor schemes.

## Slide 18
Simulation Environment: Inputs
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Simulation topology inputs:
  radius (m)
  number of nodes
  number of gateways
Fig. C: Network topologies for various number of gateways.
Notes: Simulator can generate uniformly distributed circular shape network topology with input parameters:
  radius in meter,
  number of nodes
  and number of gateways.
The tool first distributes gateways
Then, randomly places end nodes in network radius.

## Slide 19
Simulation Environment: Inputs
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Simulation inputs:
  simulation duration (s)
  packet size (B)
  packet generation rate (pps)
  SF assignment method
Notes: Global simulation input parameters are
  simulation duration in second
  packet size in Byte
  packet generation rate in packets per second
  spreading factor assignment method

## Slide 20
Simulation Environment: Outputs
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
  Simulation outputs:
  number of generated packets
  number of successfully received packets
  number of interfered packets
  number of under sensitivity packets
  network packet delivery ratio percentage
  total transmit energy consumption (J)
Notes: With these inputs the simulator produces
  number of generated packets
  number of successfully received packets
  number of interfered packets
  number of under sensitivity packets
  Network packet delivery ratio percentage,
  network throughput in bits per second
  and total transmit energy consumption in Joule
Simulator also produces prediction accuracy percentage and confusion matrix for machine learning schemes.

## Slide 21
  Link quality of a wireless system:
Sum of system gains and system losses is assumed as +7 dB
All transmissions use maximum allowed transmit power 14 dBm
Simulation Environment: Link Model
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Table I: Gateway sensitivity for different SFs [13].
Notes: Link quality of a wireless system can be expressed by the link budget
Link budget can be calculated by this formula where
  PRX is the expected receive power at the receiver
  PTX is the transmit power of the transmitter
  G SYS is the system gains such as transmitter and receiver antenna gains
  L SYS is the system losses such as transmitter and receiver line, circuit, antenna losses
  L PATH is the propagation path loss between transmitter and receiver antennas in open space
it is assumed that sum of system gains and system losses is +7 dB
it is assumed that nodes always select maximum allowed transmit power, which is 14 dBm.
If the received signal power is higher than the gateway sensitivity,
then signal can be decoded by the receiver successfully when there is no interfering transmission.

## Slide 22
  Free space propagation loss:
  Assume h = 15 m and f = 868 MHz
Simulation Environment: Link Model
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Notes: Free space propagation loss is calculated as
  Where h is the gateway altitude and f is the frequency of the signal,
  It is assumed that gateway altitude is 15 m and frequency is 868 MHz which is European ISM band frequency
With these assumptions, propagation loss calculation become

## Slide 23
Simulation Environment: Interference Model
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
It is assumed that there is no other technology interference
Simulator calculates the effect of different SF transmissions to each other
  Signal to interference plus noise ratio threshold matrix
If there are more than one interfering signal
  Cumulative sum of all interfering signal received power for each SF
Notes: In this work, it is assumed that there is no other technology interference in the network except LoRa interference
Simulator calculates the effect of different spreading factor transmissions to each other
  Signal to interference plus noise ratio threshold matrix is adopted from previous works
If there are more than one interfering signal, referenced signal must satisfy the margin for sum of all interfering signal received power for each spreading factor

## Slide 24
Simulation Results: Single Gateway
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Fig. 4 : PDR plot for various spreading factors. (r = 3000 m, GW = 1)
Fig. 5 : PDR plot for various network radii. (GW = 1, SF = SF_Lowest)
Notes: First, I will present single gateway and multiple gateway simulation results to show correctness of the simulator
These figures validate the tool we get the expected results
Here PDR plot of various spreading factor assignment schemes is shown
Increasing spreading factors, increases time on air
This increases the number of collisions thus decreases the PDR
High spreading factors gives poor PDR results as the number of nodes increases
plot for various network radii is shown
lowest spreading factor assignment scheme is used for these plots
Increasing network radius,
  increases the number of under sensitivity transmissions
  thus decreases the PDR
Nodes select higher spreading factors when they are far away from the gateway.
  Thus, higher spreading factor leads to
  longer air time,
  higher number of collisions
  and higher total transmit power consumption

## Slide 25
Simulation Results: Multiple Gateway
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Fig. 6 : PDR plot for various number of gateways. (r = 3000 m, SF = SF_Lowest)
Notes: plots for various number of gateways are shown
Increasing number of gateways in constant topology radius,
  decreases the distance between nodes and gateways
  Thus, decreases the number of collisions at gateways
  Hence, increases the PDR.
Since topology radius is small, most of the end nodes selects lowest spreading factor all the time
  Thus air time is same and total transmit power consumption is same for all plots

## Slide 26
Simulation Results: Smart SF Schemes
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Fig. 7: PDR plot for lowest and smart spreading factor schemes. (r = 5000 m, GW = 3)
Notes: Finally plot for the smart spreading factor scheme is shown, this plot is main objective and main results of this work
Both smart SVM and smart DTC schemes give better PDR than lowest spreading factor schemes when number of nodes increases.
Increasing number of nodes, increases number of interferences.
Smart schemes can only improve network performance when LoRa interference is high.
Moreover, smart schemes give better results when nodes are deployed closer to the gateway, since nodes have margin to increase their spreading factors when they are deployed closer to the gateway
If a node is far away from gateway, then smart schemes cannot increase the spreading factor to avoid interference since the assigned spreading factor is already high.
As number of nodes increases, both smart SVM and smart DTC schemes give better PDR results

## Slide 27
Simulation Results: Smart SF Schemes
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Fig. 8: Transmit energy plot for lowest and smart spreading factor schemes. (r = 5000 m, GW = 3)
Notes: As number of nodes increases, both smart SVM and smart DTC schemes consume slightly more energy than lowest spreading factor scheme,
however they give better PDR results in return
Random spreading factor scheme consumes much higher transmit power than the rest.

## Slide 28
Conclusion
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
SF assignment on network performance is investigated in detail
Factors that increase the number of collisions are evaluated
Measures that can be taken to reduce collisions are described
A discrete event simulator is developed from scratch to study SF assignment strategies
A novel method which utilizes machine learning techniques is proposed
Simulation results show smart SF methods provide promising network performance improvements especially for dense LoRaWAN networks
Notes: To summarize, in this work
Spreading factor assignment on network performance is investigated in detail
Factors that increase the number of collisions are evaluated
Measures that can be taken to reduce collisions are described
A discrete event simulator is developed from scratch to study Spreading factor assignment strategies
A novel method which utilizes machine learning techniques is proposed
Simulation results show smart Spreading factor methods provide promising network performance improvements especially for dense LoRaWAN networks

## Slide 29
Conclusion
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
As for future work
  Transmit power optimization
  Class B and Class C end node behavior
  Other machine learning methods such as reinforcement learning
  Other transmission parameters such as node id and transmission time can be included
Notes: As for future work,
  transmit power optimization can be included to the proposed smart schemes
    In this thesis, it is assumed that nodes always use maximum transmit power for uplink transmission, however nodes close to gateways can decrease transmit power to save energy
  it is also assumed that only LoRaWAN Class A end nodes are present, however Class B and Class C end node behavior can be integrated to check how extra downlink communication effects smart SF schemes
  Moreover, other machine learning methods can be investigated. Reinforcement learning could be a good candidate.
  Also, other transmission parameters such as node id and transmission time can be included to the proposed scheme in order to improve prediction performance

## Slide 30
Notes: Thank you for your attention.

## Slide 31
References
M. Centenaro, L. Vangelista, A. Zanella, and M. Zorzi, “Long-range communications in unlicensed bands: the rising stars in the IoT and smart city scenarios,” IEEE Wireless Communications, vol. 23, no. 5, pp. 60–67, October 2016.
U. Raza, P. Kulkarni, and M. Sooriyabandara, “Low Power Wide Area Networks: An Overview,” IEEE Communications Surveys Tutorials, vol. 19, no. 2, pp. 855–873, January 2017.
O. Georgiou and U. Raza, “Low Power Wide Area Network Analysis: Can LoRa Scale?” IEEE Wireless Communications Letters, vol. 6, no. 2, pp. 162–165, April 2017.
“LoRa Modulation Basics,” Semtech Corporation, Camarillo, California, USA, Tech. Rep. AN1200.22, May 2015. [Online]. Available: https://www.semtech.com/uploads/documents/an1200.22.pdf
D. Magrin, M. Centenaro, and L. Vangelista, “Performance evaluation of LoRa networks in a smart city scenario,” in 2017 IEEE International Conference on Communications (ICC), May 2017, pp. 1–7.
F. Van den Abeele, J. Haxhibeqiri, I. Moerman, and J. Hoebeke, “Scalability Analysis of Large-Scale LoRaWAN Networks in ns-3,” IEEE Internet of Things Journal, vol. 4, no. 6, pp. 2186–2198, December 2017.
D. Croce, M. Gucciardo, S. Mangione, G. Santaromita, and I. Tinnirello, “Impact of LoRa Imperfect Orthogonality: Analysis of Link-Level Performance,” IEEE Communications Letters, vol. 22, no. 4, pp. 796–799, April 2018.
A. Mahmood, E. Sisinni, L. Guntupalli, R. Rond´on, S. A. Hassan, and M. Gidlund, “Scalability Analysis of a LoRa Network under Imperfect Orthogonality,” IEEE Transactions on Industrial Informatics, pp. 1–1, September 2018.
“LoRaWAN simple rate adaptation recommended algorithm,” Semtech Corporation, Camarillo, California, USA, Tech. Rep. v1.0, October 2016.
E. Alpaydin, Introduction to Machine Learning, 2nd ed. The MIT Press, 2010.
T. Yatagan, “tugrulyatagan/simlorasf,” May 2019. [Online]. Available: https://doi.org/10.5281/zenodo.2671495
“LoRaWAN 1.1 Regional Parameters,” LoRa Alliance, San Ramon, California, USA, Tech. Rep. v1.1rB, January 2018. [Online]. Available: https://lora-alliance.org/sites/default/files/2018-04/lorawantm regional parameters v1.1rb - final.pdf
“SX1276/77/78/79 - 137 MHz to 1020 MHz Low Power Long Range Transceiver Datasheet,” Semtech Corporation, Camarillo, California, USA, Tech. Rep., August 2016. [Online]. Available: https://www.semtech.com/uploads/documents/DS SX1276-7-8-9 W APP V5.pdf
“Radio Frequency (RF) system scenarios,” ETSI, Tech. Rep. TR 136 942 V13.0.0, January 2016. [Online]. Available: https://www.etsi.org/deliver/etsi tr/136900136999/136942/13.00.00_60/tr 136942v130000p.pdf
C. Goursaud and J. M. Gorce, “Dedicated networks for IoT : PHY / MAC state of the art and challenges,” EAI endorsed transactions on Internet of Things, October 2015. [Online]. Available: https://hal.archives-ouvertes.fr/hal-01231221

## Slide 32
LoRa: Spreading Factor
Ratio between symbol and chirp rate is equal to 2SF
SF can take values between 7 and 12
SF provides tradeoff between data rate, range and power consumption
Fig. C: Spectrogram of various spreading factors (SF7 to SF 12). [1]
Fig. D: Spectrogram of an example LoRa transmission. [1]
1. Image Source: https://www.sghoslya.com/p/lora-is-chirp-spread-spectrum.html
Appendix
Notes: The ratio between symbol and chirp rate is equal to 2SF
  Spreading factor also determines data rate of a LoRa transmission
  Here Rb is bit rate in bps, SF is spreading factor, CR is error correction code rate BW is bandwidth in Hertz
  SF can take values between 7 and 12
  CR can take values between 1 and 4
When bandwidth and code rate are constant as the spreading factor increases, the data rate decreases
Higher spreading factors delivers long range at an expense of lower data rate and high power consumption

## Slide 33
LoRaWAN
Appendix
End Node (EN)
  Low power embedded device that only communicates with gateways
  Class A
    Generates uplink transmission at any time
    Only receives a period of time after an uplink transmission
    Default operation mode
    Suitable for battery powered applications
  Class B
    Periodic receive window
    Suitable for low latency applications
  Class C
    Continuous receive window
    Suitable for no latency applications
Fig. E: LoRaWAN class A, B and C TX/RX timing diagram. [1]
1. Image Source: https://witekio.com/blog/lorawan-dedicated-iot-network
Notes: LoRa has an open standard MAC layer protocol called LoRaWAN
  LoRaWAN is developed and maintained by LoRa Alliance which is an non-profit organization
There are three main LoRaWAN network entities, which are end node, gateway and network server
End node is a low power embedded device that only communicates with gateways
LoRaWAN standard defines three classes for end devices
Class A end nodes generate uplink transmission at any time
  And Only receives a period of time after an uplink transmission
  Class A is the default operation mode for end nodes
Class B end nodes extend Class A behavior by adding scheduled periodic receive windows
Class C end nodes extend Class A behavior by keeping receive window open all the time
In this thesis, only Class A end devices are considered since Class A behavior leads to the lowest power consumption and Class A is the default operation mode.

## Slide 34
LoRa: ISM Regulations
LoRaWAN operates in license free Industrial, Scientific, and Medical (ISM) bands
ISM bands are subject to radio transmission time and power regulations
Duty cycle restriction
  Limitation on percentage of air time
  1% duty cycle restriction enforces
    Single transmission cannot exceed 3.6 seconds
    Total time on air in one hour cannot exceed 36 seconds
Effective isotropic radiated power restriction
  Sets maximum allowed transmit power of a transmitter
Table B: EU863-870 ISM band LoRa channels.
Appendix
Notes: LoRaWAN operates in license free ISM bands.
ISM bands are subject to radio transmission time and power regulations
Duty Cycle Restriction is a limitation on percentage of air time.
  For example 1% duty cycle restriction enforces
  Single transmission cannot exceed 3.6 seconds
  And total time on air in one hour cannot exceed 36 seconds
Effective Isotropic Radiated Power Restriction sets the maximum allowed transmit power of a transmitter

## Slide 35
Proposed Technique: Simulation
For every transmission:
  The classifier predicts the transmission result for the lowest possible SF
  If the transmission result is predicted as interfered
    increase SF
    predict a new transmission result
  If new transmission result is classified as successful
    continue to execute with selected SF
  If no SF transmission result is predicted as successful
    select the lowest possible SF
    continue to execute
Appendix
Notes: For every transmission
  the classifier predicts the transmission result for the lowest possible SF
  If the transmission result is predicted as interfered, then the tool increases the spreading factor and predicts a new transmission result
  If the new transmission result is classified as successful, then simulator continues to execute with selected spreading factor
  If no spreading factor transmission result is predicted as successful, then the tool selects the lowest possible spreading factor again and continue to execute.

## Slide 36
Simulation Environment: Interference Model
It is assumed that there is no other technology interference
Simulator calculates the effect of different SF transmissions to each other
  Signal to interference plus noise ratio threshold matrix [33]:
  Margin between referenced signal and interfering signal to correctly decode the referenced signal
Appendix
Notes: In this work, it is assumed that there is no other technology interference in the network except LoRa interference
Simulator calculates the effect of different spreading factor transmissions to each other
signal to interference plus noise ratio threshold matrix is adopted
  Where T ij is margin between referenced signal with SF = i and interfering signal with SF = j to correctly decode the referenced signal

## Slide 37
Simulation Environment: Interference Model
If there are more than one interfering signal
  Cumulative sum of all interfering signal received power for each SF
  SINR threshold can be calculated
Packet survives from all interferences if:
Appendix
Notes: If there are more than one interfering signal, referenced signal must satisfy the margin for sum of all interfering signal received power for each spreading factor
SINR threshold can be calculated by this equation
  Where Prc,0 is received signal power of referenced signal
  Prc,l is received signal power of interfering signal for SF = j.
If a packet with SF = i satisfies the following condition for every SF = j, then packet is survived from all interferences.

## Slide 38
Simulation Environment: Software
Tool keeps an event queue
Every event is a transmission
Every transmission has
  Time
  SF
  Source
  Duration
  Status
Simulation steps:
  Every node generates an event according to their traffic generation rate
  Initially all events are in pending state
  Tool executes events
  Tool marks events statuses as transmitted, interfered or under sensitivity
  Tool calculates network PDR, throughput and transmit energy consumption
Example CLI command:
python3 main.py -r 7000 -g 3 -n 300 -s SF_Lowest -d 3600
Appendix
Notes: The tool keeps a transmission queue
Every event in this queue is a transmission
Every transmission has
  time
  spreading factor
  source
  Duration
  and status fields
First
  Every end node generates an event according to their traffic generation rate and inserts this event to event queue.
  Initially all events are in pending state
  Tool executes events one by one
  Tool marks events statuses as transmitted, interfered or under sensitivity
  Finally tool calculates network PDR, throughput and transmit energy consumption
A command line parser is developed for interacting with the tool, so the tool can be run without any programming or scripting
  Example tool command is below

## Slide 39
Prediction accuracy is not directly proportional to network PDR
Correct prediction of an interfered transmission may not increase the PDR but increases the prediction accuracy
Simulation Results
Introduction
LoRa & LoRaWAN
Related Works
Proposed Technique
Simulation Environment
Simulation Results
Conclusion
Table III: Prediction accuracy for SVM and DTC. (GW = 3)
Notes: prediction accuracy of smart SVM and smart DTC schemes are presented for various network radii and number of nodes.
Prediction accuracy is not directly proportional to network PDR
Correct prediction of an interfered transmission may not increase the PDR but increases the prediction accuracy
Smart DTC gives better network PDR results than smart SVM, even overall smart SVM prediction accuracy is higher
The distribution of different labeled data points in the dataset is strongly related to simulation parameters.
If simulation is run with small topology radius and high number of nodes, then number of interfered transmission labeled data points increases.
On the other hand, using a large topology radius in the simulation causes the number of under sensitivity transmission labeled data points to increase.
Moderately dense network parameters are chosen to make it closer to real world deployments.
With the simulation parameters utilized in this section, simulation tool usually produces imbalanced dataset.
Number of under sensitivity transmission labeled data points are less than number of successful transmission labeled data points.
Besides, number of interfered transmission labeled data points are even less than number of under sensitivity transmission labeled data points. In this case, smart DTC predicts interfered transmission labeled data points more accurately.
Correct classification of interfered transmissions yields better network PDR results, thus smart DTC scheme gives better network PDR results.