## Slide 1: 6.888 Lecture 16: Header Space Analysis
Mohammad Alizadeh
Spring 2016
Slides courtesy of Peyman Kazemian (Stanford)

## Slide 2: Digital Hardware Design
$10B tool business supports a $250B chip industry
Specification
Functional Description (RTL)
Testbench & Vectors
Functional Verification
Logical Synthesis
Static Timing
Place & Route
Design Rule Checking (DRC)
Layout vs Schematic (LVS)
Layout Parasitic Extraction (LPE)
Manufacture
& Validate
100s of Books
>10,000 Papers
10s of Classes
Notes: Let’s look at how digital hardware design works. The cost of making any mistakes here is millions of dollars, so we don’t want to make any mistake ever. There is a very well-thought design methodology, starting with specification, leading to functional description along side with test benches and test vectors. Then going through functional verification and compiling it all the way down to physical layout. And then the we test the manufactured hardware against the test bench we created to ensure consistency. Here a 10B$ industry, supports a 250$ chip industry, using a large set of tools and techniques we know about. and that is made possible through a huge amount of intellectual efforts: there are 100s of books and more than 10,000 research papers related to this topic, with 10s of classes taught at academic institutes.

## Slide 3: Software Design
Static Code Analysis
Invariant
Checker
Interactive Debugger
Model Checking
Run-time Checker
Specification
Testbench
Functional Description (Code)
$10B tool business supports a $300B S/W industry
100s of Books
>100,000 Papers
10s of Classes
Notes: Same goes in software design. We start from specification and drive the functional description (the code) along with test benches, and we use a bag of tools and techniques to test and verify our design. Again a 10B$ tool industry supports a 300B$ software industry which is based on many intellectual ideas and principles published in 100s of books, 100s of thousands of papers and thought in 10s of academic classes.

## Slide 4: Managing Networks (Today)
traceroute, ping, tcpdump, SNMP, Netflow
…. er, that’s about it.
Notes: So how do we do it in networking? How do we make networks work? Well we have ping, traceroute, tcpdump, SNMP, Netflow… and that’s about it! Where is that 10B$ tool industry to support it? Where are the intellectual ideas and classes?
Networks are made to work today by highly skilled, hard to find and well-paid talented individuals called network administrators. It is debugged through pattern matching by human rather than rigorous and automated tools. It is not surprising that it barely works.

## Slide 5: Why is network debugging hard?
Complex interaction
  Between multiple protocols on a switch/router.
  Between state on different switches/routers.
Multiple uncoordinated writers of state.
Network owner can’t…
  Observe all state.
  Control all state.

## Slide 6: Networks are kept working by “Masters of Complexity”

## Slide 7: Simple questions are hard to answer
  Can host A talk to host B?
  What are all the packet headers from A that can reach B?
  Is Group X provably isolated from Group Y?
  Are there any loops in the network?
  What happens if I remove this line in the config file?
Notes: As a result, even simple questions about a network are hard to answer.

## Slide 8: How have other fields overcome similar challenges?

## Slide 9: Communication Engineering
S
D
Frequency
Modulation
Antenna
De-
Modulation
Antenna
Band Pass Filter
Cos(wt)
Cos(wt)
Amplifier
Notes: As another example, let’s look at the field of communication systems. There is a similar problem there: given a complex system consisting of many different elements, we are interested to know how an input signal will be received at the receiver. Let’s look at an example system. Consider this system that consists of different components such as amplifier, modulator and demodulator, Antenna and filter. Our goal is to find out how the receiver will receive the signal. To solve the problem we first find the Fourier representation of the input signal. This gives us a simple and common way to represent any signal from voice and video to data. Then we model each component of the system by its transfer functions. The beauty of this approach is that once we have the transfer function of these components, they all look the same: we no longer care about whether it is an antenna, an amplifier or the transmission medium. Then we apply the input signal to the transfer functions one by one and find the signal at the receiving end.

## Slide 10: Digital Hardware Design
clock
A
B
out
Notes: Also, in the digital circuit design, instead of thinking in terms of transistors, we have higher level logical Gate abstraction.

## Slide 11: Digital Hardware Design
clock
A
B
out
Notes: Once we have logical gates, then we have boolean algebra, karnu map, queen-mcklusky and a whole bag of higher level tools and techniques to design and verify our system. I am going to tell you how we can do the same thing in networking.

## Slide 12: “Systems” Framework for Networks
Input ACL
IP table
Output ACL
ARP
Table
MAC
Table
Spanning
Tree
MPLS
Mappings
Filtering Rules
IP Table
MAC
Table
Input ACL
IP table
Output ACL
ARP
Table
MAC
Table
Spanning
Tree
Spanning
Tree
VLAN
Table
MAC
Table
Notes: So that instead of looking at different types of boxes, from different vendors, running different protocols distributed over multiple tables…

## Slide 13: “Systems” Framework for Networks
Input ACL
IP table
Output ACL
ARP
Table
MAC
Table
Spanning
Tree
MPLS
Mappings
Filtering Rules
IP Table
MAC
Table
Input ACL
IP table
Output ACL
ARP
Table
MAC
Table
Spanning
Tree
Spanning
Tree
VLAN
Table
MAC
Table
Notes: We look at a simple unified representation of packets and networking boxes. I want to exploit the fact that forwarding state of network determines the behavior of network and use it as a foundation for systematic analysis of network.

## Slide 14: Header Space Analysis

## Slide 15: Header Space Framework
Step 1:
  Ignore protocol dependent meaning of header bits and see it as a flat sequence of 0s and 1s.
  Model a packet as a point in {0,1}L space – The Header Space
0101..1
1010..1
0010..0
0010..0
Data
SRC MAC
DST MAC
DST IP
SRC IP
0101..11010..10010..00010..0
Header
Data
L
010xxx011..x001xxxxx01110
Notes: The first step is to model a packet based on its header as a point in {0,1}L space, which we call the header space. The idea here is that we look at packet headers a a flat sequence of 0s and 1s, without any protocol specific meaning for those bits. We don’t care whether the 32 bits corresponds to IP source or destination. That’s related to protocols. Then based on value of those bits, we map the packet to a point in the header space. Here we need to choose L large enough to contain all bits in the header. Similarly, a flow that has some wildcard bits in it, will corresponds to a region in the header space. Like Fourier transform in communication systems, the header space representation give us a simple and unified view of all packets.

## Slide 16: Header Space Framework
Step 2 – Model all networking boxes as transformers of header space
Packet
Forwarding
1
2
3
0xx1..x1
Match
+
Send to port 3
Rewrite with 1xx011..x1
Action
11xx..0x
+
Send to port 2
Rewrite with 1x01xx..x1
1110..00
1101..00
Transfer Function:
Why is the output a set of packets?
Notes: The second step is to model all networking boxes as transformer of header space. Here I am showing a simple packet forwarding element consisting of 3 ports, and I also show the header space corresponding to each port. We know that we can represent the forwarding functionality of this box by a set of rules. Each rule consists of a match which tell us which packets match on this rule and an action which tell us how the matching packets are sent to output. The match basically corresponds to a region in the input port header space and the action shows how that region is transformed to output. Similarly if we have more rules, we will have more match regions that is transformed to output header space….

## Slide 17: Transfer Function Example
IPv4 Router – Forwarding Behavior
  172.24.74.x Port1
  172.24.128.x Port2
  171.67.x.x Port3
1
3
2
(h,1) if dst_ip(h) = 172.24.74.x
(h,2) if dst_ip(h) = 172.24.128.x
(h,3) if dst_ip(h) = 171.67.x.x
T(h, p) =
Notes: Mask notation 101…10xxx…xx
Explain why we have prefixes. Maybe tell each subnet is for a department: chemistery, cs, etc

## Slide 18: Transfer Function Example
IPv4 Router – forwarding + Time to Live (TTL)
  172.24.74.x Port1
  172.24.128.x Port2
  171.67.x.x Port3
1
3
2
(dec_ttl(h),1) if dst_ip(h) = 172.24.74.x
(dec_ttl(h),2) if dst_ip(h) = 172.24.128.x
(dec_ttl(h),3) if dst_ip(h) = 171.67.x.x
T(h, p) =

## Slide 19: Transfer Function Example
IPv4 Router – forwarding + TTL + MAC rewrite
  172.24.74.x Port1
  172.24.128.x Port2
  171.67.x.x Port3
1
3
2
(rw_mac(dec_ttl(h),next_mac) , 1) if dst_ip(h) = 172.24.74.x
(rw_mac(dec_ttl(h),next_mac) , 2) if dst_ip(h) = 172.24.128.x
(rw_mac(dec_ttl(h),next_mac) , 3) if dst_ip(h) = 171.67.x.x
T(h, p) =

## Slide 20: Other Examples:
Rewrite: rewrite bits 0-2 with value 101
  (h & 000111…) | 101000…
Encapsulation: encap packet in a 1010 header.
  (h >> 4) | 1010….
Decapsulation: decap 1010xxx… packets
  (h << 4) | 000…xxxx
TTL Decrement:
  if ttl(h) == 0: Drop
  if ttl(h) > 0: h – 0…000000010…0
Load Balancing:
  LB(h,p) = {(h,P1),…(h,Pn)}
Notes: * Encapsulation is wrapping a packet into a new header
* Decapsulation is to remove the outermost header
* Using these action we can model the vast majority of networking boxes.

## Slide 21: Composing Transfer Functions
T1(h, p)
R1
R2
R3
By composing transfer functions, we can find the end to end behavior of networks.
Notes: * Tell them that previously people had to log into boxes, understand different notion, from different protocols and different vendors.
By composing transfer functions, we can find the end to end behavior of networks and the faith of packets as they traverse in the network. Let’s look at one example. Consider this packet arriving at box R1. by applying the transfer function of R1 to the packet, we can see the packet reaches to R2. we then apply the transfer function of R2 to the result, and see the packet reaching R3. repeating the same process, we can see that applying the transfer functions sequentially to the input packet, which is equivalent to composing those transfer functions, will show the faith of the packet after going through the network.
Therefore, for packet between these two ports, we can model the forwarding behavior of the network by a black box, withT3T2T1 transfer function. Remember that without this mechanism, we had to log into every box and comprehend the overall behavior from different tables running different protocols and belonging to multiple vendors.

## Slide 22: Inverting Transfer Functions
Tell us all possible input packets that can generate an output packet.
T(h,p)
Input Header Space
Output Header Space
T-1(h,p)
Notes: The other property of transfer functions is that we can invert them, and the inverse tell us all possible input packet that can generate an output. I am not gonna give you detail example of how to find inverse, but conceptually it means that if we have these input header space regions that are mapped to the output regions by transfer function, the inverse if of transfer function replace their positions, mapping output regions to input regions. Even it may be the case that a point like this is inverted back to two points, but that is fine, since inverse of transfer function, like the transfer function itself can have a set as output.

## Slide 23: Header Space Framework
Step 3- Header Space Set Algebra.
  Intersection
  Complementation
  Difference
  Check subset and equality condition.
Every region of Header Space, can be described by union of Wildcard Expressions. (example: 10xx U 011x)
Goal: do set operation on wildcard expressions.
Notes: As the 3rd step, we want to define set operations on regions of header space or header space objects. We want to find intersection, complementation, difference and check for subset and equality conditions. As you will see when develop algorithms later in the talk, these are important constructs. For example when we check if two slice of networks are isolated or not, we should makes sure that their header space definition does not intersect, so we need a way way for checking that. Also in the loop detection algorithm, when we want to check if the loop is infinite or not, we need to check if two regions are subset of each other or not.

## Slide 24: HS Set Algebra- Intersection
Bit by bit intersect using intersection table:
  Example:
  If result has any ‘z’, then intersection is empty:
  Example:
wildcard
empty

## Slide 25: Algorithms

## Slide 26: Finding Reachability
All Packets that A can use
to communicate with B
All Packets that A can possibly
send to box 2 through box 1
All Packets that A
can possibly send
Box 1
Box 2
Box 3
Box 4
A
B
T1(X,A)
T2(T1(X,A))
T4(T1(X,A))
T3(T2(T1(X,A)) U T3(T4(T1(X,A))
T-13
T-13
T-14
T-12
T-11
T-11
All Packets that A can
possibly send to box 4
through box 1
Notes: The first problem we want to look at, is finding reachability between two hosts in the network. We want to find out whether A can talk to B and if so, what are all packet header that will reach B.
To do that, we start by injecting test packet with wildcard in all bit positions into this simulated network. An all-x test packet is a packet whose bits are all wildcarded, and it represent the set of all possible packet headers that A can generate.
I want to emphasize that we don’t actually send any packet in the actual network, we get a complete snapshot of network and generate transfer function for each box in the network and use it for our analysis.
We apply the all-x packet to the transfer function of box 1, and gets some header space regions passed through the box, so we get the headers at the output of box1. we then apply the result to second transfer function – get the output header space after 2 hops, and finally to the 3rd transfer function giving us the ultimate results….

## Slide 27: Finding Loops
Is there a loop in the network?
  Inject an all-x test packet from every switch-port
  Follow the packet until it comes back to injection port
Box 1
Box 2
Box 3
Box 4
T1(X,P)
T2(T1(X,P))
T3(T2(T1(X,P)))
T4(T3(T2(T1(X,P))))
Original HS
Returned HS
T-14
T-13
T-12
T-11
Notes: … Now if we want to see if the returned header space region will loop in the next round or not, we should apply the inverse of transfer function to trace the returned header space back to its origin and find out what part of the original all-x test packet could generate the loop. We call this the original header space and the blue region, the returned header space. The idea here is that, from all packet headers, only this orange region can generate loop, and it will come back to injection port in the form of this blue region.

## Slide 28: Finding Loops
Is the loop infinite?
Finite Loop
Infinite Loop
?
Notes: Now the answer to this question depends on the situation of these two regions – if the two regions don’t intersect, the loop is finite. Consider any point in the orange region. After it goes through the loop, it comes back as a point in the blue region. But the points in the blue region can not loop – therefore the loop is not infinite.
However in the scenario that the returned header space is completely within the original header space, the loop will be infinite. Because now any point in the orange header space will go through the loop and map back to a point in the blue region which is still inside the orange region – so the loop will continue.
Finally, if there is a partial intersection between the two regions, we need to do more work. First, the blue region outside the orange region can not loop, because it falls into the first category. So we focus only on the intersection. For this intersection, we use the inverse transfer function technique to find out what part of the original header space or the orange region, is generating this region. By doing this, we see that the problem is reduced to first scenario, and therefore the loop is finite. However if we ended up in the same scenario again, we just keep repeating this process until, we either end up in one of the first two cases or the regions shrinks to empty.

## Slide 29: Checking Isolation of Slices
How to check if two slices are isolated?
  Slice definitions don’t intersect.
  Packets don’t leak after forwarding.
Notes: Now let’s get back to the original question – how to check if two slices are isolated?
Let’s imagine in this example network, we have a red slice defined as shown. The first check, is to make sure that slice definitions don’t intersect. We can use intersection operation of HSA to this check. The red and blue slice pass this check.
The second check is to make sure that packets don’t leak after forwarding. To check for that, we apply the header space definition of each slice to the transfer function of network, to find the image of slice under network transformation, and that image should not intersect with any other slices, because the image shows us how packets in one slice will look like after one hop of forwarding. In this case, they do, and therefore the two slice are not isolated.

## Slide 30: Header Space Library (Hassel)

## Slide 31: Header Space Library (Hassel)
Two versions – Python and C.
Foundation Layer
  Implements Header Space and Transfer Function objects.
Application Layer
  Reachability, Loop Detection and Slice Isolation checks.
  < 100 LoC for these checks.
Parser (only available in Python)
  CLI Parsing tool for Cisco IOS, Juniper Junos and OpenFlow table dump.
    Example: for Cisco IOS, reads IP table, ARP table, MAC table, Spanning tree output and Config file.
  Keeps mapping from TF Rule to CLI line number.
Available online: git clone https://bitbucket.org/peymank/hassel-public.git
Notes: We implemented Header space library originally in Python and later on, our summer intern, Michael rewrote the library in C. Hassel consists of foundation layer that does implement Header Space and Transfer function objects. Then on top of that, the application layer uses this foundation to check such as reachability check, loop detection check and slide isolation check. The nice thing is that because of the powerful abstraction provided by Header Space and transfer function, these checks are very simple to implement, and take less than 100 line of code.
The library also includes a parser for cisco IOS, Juniper Junos and OpenFlow table dump, which is useful for generating transfer function based on actual state of devices.

## Slide 32: Optimizations: 10,000X Speedup
IP Table compression
Lazy subtraction
Dead object deletion
Lookup based search
Lazy TE evaluation

## Slide 33: Stanford backbone network
Loop detection test
Vlan RED Spanning Tree
Vlan BLUE Spanning Tree
Owns 6 x /16 IP domains.
~750K IP fwd rule.
~1.5K ACL rules.
~100 Vlans.
Vlan forwarding.
Notes: … we got a complete snapshot of all the state in the network such as IP forwarding table, ARP, MAC table, spanning tree state and ACL configs and used Hassel parser to generate the transfer functions for each box and used it to run a loop detection test.

## Slide 34: Limitations
When I add a new forwarding rule, how can I dynamically check in real-time if it will violate my network policy?
How do I track down the source code that was the root cause of a data plane error?
Is the network causing poor performance or the server? Are QoS settings to blame, poor load balancing, etc?
If switch hardware is malfunctioning, how will I know? How will I identify the switch/rule?

## Slide 35: Related Research
Policy
Control
Program
Control
Plane
Dynamic troubleshooting to Identify root cause
Formal specification languages
Static checking of lowest level design
NETWORK
Frenetic, NetCore, Pyretic, Procera, … [2012]
Anteater, HSA [2011]
Dynamic checking of lowest level design
Veriflow, NetPlumber [2012]
ATPG [2012], NetSONAR [2013]
WWW, ndb [2012]
Consistent
Updates
(several)
Packet forwarding